## Slide 1: Autonomous Robots
Sensors

## Slide 2: Sensors
Kinematics, Dynamics, Control all describe the state of the robot system and provided means of influencing it
Path Planning provides a means of determining the path/actions the system will be taking to reach a goal without collisions
All of these made the assumption that we knew the state of the system (position, velocity, etc.)
  To determine the state, we need sensors
Notes: Active sensors transmit their own signal and can thus be engineered in such a way that it is easy to detect and extract the information (e.g. transmission in a frequency band or with a modulation that occurs rarely (or never) in nature).
Extracting the information is then independent of what is actually in the environment (objects, etc.). All that has to be done is looking for the special signal and compute either time of flight or to triangulate the (known) signal.
But there are drawbacks. Active transmission can interfere both with other sensors and with objects or entities in the environment. E.g. sonar and dogs sometimes do not go together that well.

## Slide 3: Internal vs External Sensors
Sensors can be used to measure something internal to the robot or external with respect to the world
Internal sensors do not require any information from outside the system to measure aspects of the state of the system, e.g.
  Rotation sensors to measure motor angles
  Inertial measurement units to measure acceleration and rotation
  Battery state sensors
Notes: Active sensors transmit their own signal and can thus be engineered in such a way that it is easy to detect and extract the information (e.g. transmission in a frequency band or with a modulation that occurs rarely (or never) in nature).
Extracting the information is then independent of what is actually in the environment (objects, etc.). All that has to be done is looking for the special signal and compute either time of flight or to triangulate the (known) signal.
But there are drawbacks. Active transmission can interfere both with other sensors and with objects or entities in the environment. E.g. sonar and dogs sometimes do not go together that well.

## Slide 4: Rotation Sensors
Rotation sensors are important to measure the state of the motors and thus the joint angles
  Simplest rotation sensor is using a potentiometer
    Measures angle using a resistor/voltage divider
      Has a gap, i.e. can not measure full 360 degrees
      Resistor is temperature sensitive, i.e. heating changes readings
      Friction causes wear
      Need to keep track of the number of rotations
Notes: Active sensors transmit their own signal and can thus be engineered in such a way that it is easy to detect and extract the information (e.g. transmission in a frequency band or with a modulation that occurs rarely (or never) in nature).
Extracting the information is then independent of what is actually in the environment (objects, etc.). All that has to be done is looking for the special signal and compute either time of flight or to triangulate the (known) signal.
But there are drawbacks. Active transmission can interfere both with other sensors and with objects or entities in the environment. E.g. sonar and dogs sometimes do not go together that well.

## Slide 5: Rotation Sensors - Encoders
Encoders use either optical detectors or magnetic switches to produce a digital signal corresponding to rotation
  Absolute encoders use multiple rings to identify an absolute orientation
    Need to keep track of full rotations
    Range is limited by the number of rings (and thus detectors)
Notes: Active sensors transmit their own signal and can thus be engineered in such a way that it is easy to detect and extract the information (e.g. transmission in a frequency band or with a modulation that occurs rarely (or never) in nature).
Extracting the information is then independent of what is actually in the environment (objects, etc.). All that has to be done is looking for the special signal and compute either time of flight or to triangulate the (known) signal.
But there are drawbacks. Active transmission can interfere both with other sensors and with objects or entities in the environment. E.g. sonar and dogs sometimes do not go together that well.

## Slide 6: Rotation Sensors - Encoders
    Need to read it fast enough to not miss any counts
    Require a way to identify the direction of rotation
      Direction can be determined by using two detectors offset by half the width of a segment
        Quadrature encoder
  Incremental encoders use only one rings to count the incremental change in orientation
    Need to calibrate/zero the state before counting
Notes: Active sensors transmit their own signal and can thus be engineered in such a way that it is easy to detect and extract the information (e.g. transmission in a frequency band or with a modulation that occurs rarely (or never) in nature).
Extracting the information is then independent of what is actually in the environment (objects, etc.). All that has to be done is looking for the special signal and compute either time of flight or to triangulate the (known) signal.
But there are drawbacks. Active transmission can interfere both with other sensors and with objects or entities in the environment. E.g. sonar and dogs sometimes do not go together that well.

## Slide 7: Rotation Sensors - Encoders
Optical encoders are most common in robot systems
  Optical encoders can have finer gradations for sectors than magnetic encoders
  Optical encoders are less influenced by magnetic fields from motors or temperature changes

## Slide 8: Rotation Sensors - Resolvers
Resolvers can measure angle using magnetic fields
    Can be used to measure velocity more directly
    But is significantly effected by additional magnetic fields produced by the motors
  Magnetic field induces an oscillating field
    Can measure the angle without discretization

## Slide 9: Inertial Measurements
Other things about the state of the system that can be measured purely internally are dynamic forces and with them accelerations and orientations
  Accelerometers can measure the
  effect of accelerations on a mass
    Displacement of the mass is
    proportional to acceleration
  MEMS accelerometers sensors to
  measure tension in a beam on the chip

## Slide 10: Inertial Measurements
Gyroscopes can measure the gyroscopic effect or the effects of centrifugal and coriolis forces effect of accelerations on a mass
  Mechanical gyroscopes use the fact
  that rotating masses stabilize the
  rotation axis to measure orientation
  MEMS gyroscopes measure centrifugal or coriolis forces cause by the
  rotation of a mass on the chip
    Measure rotational velocity (not
    orientation (rate gyros)

## Slide 11: Inertial Measurements
  Optical Gyroscopes use the time difference caused by the rotation on the light traveling through a curled fiber
    Measure the phase shift between
    split beams traveling two different
    routes
    Require no moving parts
    Can be very precise but need to be
    careful to avoid phase-locking

## Slide 12: Internal vs. External Sensors
Internal sensors can measure the orientation of joints and accelerations and rotational velocities
  Odometry will drift over time when errors in these measurements accumulate
    Errors in position estimates from internal sensors only tend to accumulate over time
    The system will eventually get lost
External sensors measure properties of objects in the environment
  Errors in their measurements do not accumulate

## Slide 13: Global Positioning System (GPS)
Consists of a satellite-based navigation system made up of a network of 24 satellites.
GPS positioning information can be improved by obtaining additional information from fixed ground facilities. These enhancement strategies are referred to as Differential GPS and commonly uses the WAAS (Wide Area Augmentation System)
http://www.pocketgpsworld.com/howgpsworks.php
http://plane.ardupilot.com/wiki/
common-gps-how-it-works/

## Slide 14: Limitations of GPS
Ionospheric perturbations and magnetic storms (solar activity) can cause signal delays. This can be partially compensated using SBAS and L1 / L2 decoding.
Multipathing is causing GPS position errors that are difficult to detect and compensate for. Multiple GNSS receivers are better suited to filter out multipathing thanks to a higher number of visible satellites at the same time.
http://plane.ardupilot.com/wiki/
common-gps-how-it-works/

## Slide 15: Proximity Sensors
Proximity sensors measure the distance to objects in the environment
  Laser range finding (LADAR)
  Radar
  Machine Vision
  Ultrasonic
  Infrared
  Tactile sensor

## Slide 16: Tactile sensors
Tactile sensors are basically bump sensors. They are mechanical devices that close an electromechanical switch.
The switch closure acts as a binary input to the control system.
Typically used in small low-cost system. Requires low vehicle speeds and mass. Used frequently in biologically inspired behavior-based systems.
http://www.wireless-earth.de/private/mindstorms_eng.html
http://ni.www.techfak.uni-bielefeld.de/robotics

## Slide 17: Infrared Sensors
IR rangers use triangulation and a small linear CCD array to compute the distance and/or presence of objects in the field of view.
The basic idea is this: a pulse of IR light is emitted by the emitter. This light travels out in the field of view and either hits an object or just keeps on going.
In the case of no object, the light is never reflected and the reading shows no object. If the light reflects off an object, it returns to the detector and creates a triangle between the point of reflection, the emitter, and the detector.
Low-cost, simple to implement, relatively short range. Work best in controlled lighting. Requires the linearization of the sensor output.
http://www.active-robots.com/products/
robonova/robonova-sensors.shtml
www.wanyrobotics.com/.../infrared-range.jpg
http://www.acroname.com/robotics/info/articles/sharp/sharp.html#e2

## Slide 18: Ultrasonic Sensors
Ultrasonic sensors generate high frequency sound waves and evaluate the echo which is received back by the sensor. Sensors calculate the time interval between sending the signal and receiving the echo to determine the distance to an object.
Relatively inexpensive, simple to implement, good for short distance ranging.
Subject to cross-talk between multiple transmitter / receiver pairs
img.alibaba.com/photo/209455902/TS601dt_ultra...
www.uni-koblenz-landau.de/.../images/robbie6

## Slide 19: Laser range finder
Uses a laser beam to determine the distance to a reflective object.
Detects the time of flight of a laser pulse sent in a narrow beam towards an object and measures the time taken for the light to be reflected back to the sensor.
Sensor resolution is determined by the brevity of the pulse and the speed of the light detector.
Doppler effect techniques can be used to determine the relative motion and velocity of the target.
Opti-Logic RS100 unit

## Slide 20: Laser Detection and Ranging (LADAR)
Also know as LIDAR (Light Detection and Ranging)
These systems use the same basic technology as laser range finders with the exception that the laser beam is steered in one or two axes.
LADAR can be used to create two and three dimensional maps of the physical environment.
The system’s laser, scanner & optics, and photodetector & receiver electronics all influence the range, speed, and resolution of the LADAR system.
users.soe.ucsc.edu/~manduchi/Media/Ladar.jpg
www.wired.com/.../2008/01/spawar/10_mapper.jpg

## Slide 21: Laser Detection and Ranging (LADAR)
Negative Obstacles create a challenge for all sensing techniques.
Sensors tend to be placed to the front and as high as possible on the vehicle.
The CMU Crusher system uses multiple LADAR sensors to create a dynamic 3-D map of its environment

## Slide 22: 2D LIDAR / ToF Depth Cameras
Time-of-flight cameras compute the distance of a part of the object by measuring the time it takes for light to travel from a light source to the individual pixel
  Emit modulated light near lens
    Modulation changes intensity at a rate of around 15-30 MHZ
  Compute time-of-flight based on phase shift in modulation
    Eliminates the need to measure at 1/100
Modulated
Illuminator
TOF
Camera
Objects
Phase Shift
Calculation

## Slide 23: Radar
An object detection system that uses electromagnetic waves to identify the range, altitude, direction of both moving and fixed objects.
The term RADAR was coined in 1941 and stands for radio detection and ranging.
Used primarily in larger UAV and USV systems
http://gcn.com/blogs/emerging-tech/2014/06/uav-radar-sense-and-avoid.aspx

## Slide 24: Machine Vision
Machine vision systems process images acquired with cameras in order to produce a representation of objects in the world.
Computer algorithms are used to analyze patterns of pixels values provide by the image sensor.
By identifying and classifying groups of pixels as an obstacle, machine vision can be used to generate information that supports path planning or opportunistic motion behaviors.
www.roborealm.com/.../obstacle_scene_1.jpg