## Slide 1: Autonomous Robots
Robot Path Planning

## Slide 2: Path Planning
Kinematics allows to describe the geometry and configuration of a robot
  Enables computation of robot configurations
  Allows to relate multiple positions and robots
Dynamics and Control allows to produce appropriate movements for the robot
  Provides the ability to move to a desired configuration in a stable fashion
Path planning is concerned with computing the desired configurations that the robot should move through to achieve a task
Notes: This is just for a small recap how path planning relates to the previous material

## Slide 3: Path Planning
Path planning deals with the generation of movements from A to B without collisions
  Inverse kinematics could be used to generate the movement endpoint for a robot arm followed by using PD control to move to that point
    Does not work for mobile robots since an entire path has to be computed (an endpoint does not contain the information necessary to get there)
    Movement in a straight line to the point would not necessarily be collision free
Notes: Inverse kinematics can not be used to compute a goal for a mobile robot because its reaching a goal depends on a complete path calcualtion

## Slide 4: Path Planning
How to move the robot from a configuration (position and orientation) A to a configuration B without hitting arbitrarily shaped obstacles
  Shape of robot makes this more complicated
  Movement constraints for non-holonomic robots lead to complications
Notes: General path planning deals with the generic movement of a robot or part. This includes assembly operations such as combining a screw and a nut and can thus be highly complicated.

## Slide 5: Configuration Space
The shape of the robot makes it more difficult to plan a path since no part of the robot can hit an obstacle
  Robot takes up a volume in Cartesian space
Configuration space is the space spanned by the degrees of freedom of the robot
  A point in configuration space describes the complete geometry of the robot
  In Configuration space the robot can be reduced to a single point
Notes: Configuration space allows the robot to be reduced to a point. For a robot arm the configuration space is described in terms of the robot’s joint angles. For a mobile robot it is described in terms of the robot’s location and orientation.

## Slide 6: Configuration Space
In Configuration space the robot can be reduced to a point by extending the obstacles appropriately
  A round, holonomic mobile robot can be represented in a 2D configuration space
  Other robot geometries can only be addressed accurately in a 3D configuration space (position and orientation)
Notes: To expand obstacles simply trace the robot geometry around the obstacle and mark the center of the robot.

## Slide 7: Configuration Space Motion Planning
Path planning is most of the time conducted in configuration space
  Robot can be reduced to a single point
    For a mobile robot by extending obstacles in a cartesian space
    For a robot arm configuration space is described in terms of the robot’s degrees of freedom (i.e. for a robot arm with 6 DOF the configuration space is 6 dimensional), naturally reducing the robot to a point. Obstacles have to be mapped into this space.
Notes: To expand obstacles simply trace the robot geometry around the obstacle and mark the center of the robot.

## Slide 8: Configuration Space
Mapping obstacles into configuration space can be performed for any vehicle geometry
  For vehicles that can change shape this can look more complex

## Slide 9: Basic Motion Planning Problem
Basic Motion Planning Problem in Configuration Space is a simplified path planning problem
  Solid robot reduced to a single point (by extending obstacles appropriately)
  Only static obstacles
  Holonomic robot
  Only collision free paths are allowed
Notes: The basic motion planning problem is a simplification where obstacles have to be static and the robot holonomic (i.e. it can move in any direction). These assumptions make path planning simpler because motions can be planned for a point and obstacles are not allowed to move.

## Slide 10: Path Planning Approaches
Different frameworks exist for path planning
  Roadmap approaches
    Construct a set of “roads” that the robot can move on
    Find a sequence of roads that lead from start to goal
  Cell Decomposition approaches
    Decompose the space into obstacle cells and free space cells
    Find a sequence of connected free space cells such that the start is in the first and the goal in the last
  Potential Field approaches
    Design a numeric function over the configuration space with the goal at a minimum and obstacles at a maximum
    Perform gradient descent to reach the goal

## Slide 11: Properties of Path Planners
Path planners can have a number of important properties:
  Completeness
    A path planner is complete if it always finds a path if it exists
  Correctness
    A path planner is correct if any path that it finds is collision free and executable
  Optimality
    A path planner is optimal if the paths it generates optimize some property (e.g. time, distance, etc.)
Notes: These properties are important and we will analyze the path planners we cover for them.

## Slide 12: Autonomous Robots
Robot Path Planning:
Roadmap Approaches
Notes: From now on we will focus on the basic path planning problem and polygonal obstacles.

## Slide 13: Roadmap Approaches
Construct a set of intersecting roads (path segments) and determine the path by finding a sequence of roads that lead from the start to the goal.
  Similar to map-based navigation
  First step requires the construction of a finite set of roads
  Once roads are constructed a path can be find using a search process over the map
Notes: Roadmap approaches work like navigation with a street map except that the roads have to be constructed first.

## Slide 14: Roadmap Approaches
How roads are constructed is one of the most important differences between different roadmap approaches
  How can one find a set of roads that includes the start and the goal ?
  What properties should the road map have ?
Notes: Road construction is the most complex part of roadmap based path planners

## Slide 15: Visibility Graphs
Road construction
  Connect all corners of the polygonal obstacles and the robot and goal as long as they are visible from each other.
Path Search
  Find a sequence of road segments that connects start and goal using best first search (expanding the shortest path first)
1
2
3
4
5
6
7
8
9
10
11
12
16
17
18
13
14
15
19
20

## Slide 16: Visibility Graphs
Complete ?
  Yes. If there exists a path then there exists one that is constructed of straight line segments connecting obstacle surface points
Correct ?
  Yes. However, paths touch obstacles (note they do not collide). Paths have no safety margin
Optimal ?
  Yes. If best first search is used, the shortest distance path will be found
Notes: The largest problem with visibility graphs is that they do require the robot to touch obstacles. As a result any deviation from the path could cause a collision.

## Slide 17: Voronoi Diagrams
Voronoi Diagrams attempt to construct roads with maximal safety margins
  Roads are equidistant from the two nearest obstacle features
  There is a road between any two features (corners and edges) of the polygonal obstacles
    Road segments between two edges are straight line segments
    Road segments between two corners are straight lines
    Road segments between a corner and an edge are curves
Notes: These were covered last class

## Slide 18: Voronoi Diagrams
Road construction
  Construct road segments that are equidistant to the two nearest obstacle features (including the workspace boundaries)
  Connect start and goal to the nearest road
Path search
  Find a sequence of road segments that leads from start to goal

## Slide 19: Voronoi Diagrams
Complete ?
  Yes. If there exists a path then there exists one that is at every point equidistant from the two nearest obstacle features
Correct ?
  Yes. Paths locally keep maximum distance from obstacles and will not collide
Optimal ?
  No. Paths are not optimal in terms of length, time, or safety (the search for a path does not look for maximum clearance)
Notes: The paths generated are not optimal in terms of distance to the nearest obstacles since the search does not include any criterion (or preference) for paths with such a property. The distance holds only locally.

## Slide 20: Visibility Graphs vs. Voronoi Diagrams
Visibility graphs result in optimal paths in terms of distance
  Paths are “unsafe” because they graze obstacles
Roads for Visibility graphs are easier to construct
Voronoi diagrams generate safer paths
  Paths keep locally maximal distance from obstacles
  Paths tend to be smoother
Both approaches generate paths that contain sharp corners which are difficult to execute for a real robot
  Dynamically require the robot to stop
Notes: Both methods have their advantages. Voronoi diagram results in higher safety, Visibility graph is easier and results in minimum distance paths.

## Slide 21: Voronoi Diagrams
Approximate Voronoi diagram can be generated easier using distance propagation methods
  Simultaneously starting wave fronts from all obstacles, record the points at which two wave fronts meet for th first time
    In practice this requires a discretization of the configuration space.
Notes: Wave propagation provides a means of computing voronoi diagrams more efficiently

## Slide 22: Roadmap Approaches
Roadmap-Based path Planning
  Advantages:
    Well defined movement paths
    Path can be found fast using search
  Disadvantages:
    Roadmap construction can be time consuming:
      Visibility graphs with large numbers of obstacles is expensive
      Voronoi diagrams are difficult to compute
    Visibility graph and Voronoi diagram do not translate well into configuration spaces with more than 2 dimensions
Notes: Both visibility graph and voronoi diagram do not work in 3D. There are other roadmap approaches though that construct roads randomly and can address higher dimensional configuration spaces