## Slide 1: Autonomous Robots
Traditional and Behavior Based Control

## Slide 2: Traditional and Behavior Based Control
Path Planning provides a means to autonomously generate a path from a start to a goal
  Requires complete knowledge of world and task
    Replanning is needed if anything changes
Task-level control often has to consider more complex task conditions
  Path planning would require very high-dimensional configuration spaces
  Other approaches are needed to deal with unknown aspects of the task or environment

## Slide 3: Cybernetics
Complex modeling and planning can solve complex tasks
Cybernetics – simple reactive sensor and control loops can “solve” complex tasks
    E.g. Braitenberg’s vehicles
        Simple vehicles with light sensors and motors
        Control is direct mapping from sensors to actuators
        Minimal logic is used to modulate reflexes

## Slide 4: Braitenberg’s Vehicles
Simple vehicles by modulating sensor-motor loop
  Faster if closer to light
  Turns away from light and stops
  “Coward” or “Fear”
  Faster if closer to light
  Turns towards the light
  “Aggressive”

## Slide 5: Braitenberg’s Vehicles
Simple vehicles by modulating sensor-motor loop
  Slower if closer to light
  Turns towards the light
  “Love”
  Slower if closer to light
  Turns away from the light
  “Explorer”
© F. Roth, J. Heinzle, A. Duff, J. Conradt

## Slide 6: Cybernetics and Braitenberg’s Vehicles
Complex autonomous behavior can be built by from cybernetic reflexes or reactions
  E.g. combining basic Braitenberg’s vehicles can address complex tasks
© E. Araujo

## Slide 7: Autonomous Control Modes
Autonomous control architectures range in terms of the way they solve control problems
  Reflexive Control
    Direct stimulus-response mappings
    No memory or map used
  Reactive Control
    Mapping from short-term local knowledge to control
  Deliberative Control
    Planning based on available information
Reflexive
Deliberative
Reactive

## Slide 8: Reactive vs. Deliberative Control
Deliberative control uses a traditional sense, model, plan, execute cycle
Reactive control uses limited, distributed local models and distributed control
  End-to-end tasks
  Modeling bottleneck
  Execution of solution
  Fast reaction
  Task solution unknown
  Difficult for complex tasks

## Slide 9: Deliberative Control
Deliberative autonomous control follows a sense, model, plan, execute cycle
  Sensing: use sensors to observe the state of the Robot and of the environment
  Modeling: Include the new information into a complete model of the Robot and the environment
  Planning: Given the task goal, use a planning technique to come up with a solution plan
  Executing: If a plan was found, perform the next step of the plan

## Slide 10: Behavior-Based Control
Reflexes are direct mappings from sensors to motors
  No models of the system or environment
  No filtering and integration of sensor data
Reactive behaviors are more complex
  Local, simple models
  Accumulation, filtering, and integration of sensor data over time
  Fast reactions based on the model

## Slide 11: Reactive vs. Deliberative Control
Reflexive
Deliberative
Reactive
Reaction
speed
Model
dependence
Predictability
Robustness
Task
complexity

## Slide 12: Behavior-Based Architectures
Behavior-based control can address situation without sufficient information
© Villanova ASV

## Slide 13: Behavior-Based Architectures
Behavior-based systems combine a number of reactive behaviors
  Composition combines the behaviors either in a competitive or a collaborative fashion
Composition
Motors
Sensors
Behavior n
Behavior 3
Behavior 2
Behavior 1
.
.
.

## Slide 14: Behavior-Based Architectures
Competitive composition mechanisms
  Priority-based – highest priority active behavior drives the system
    E.g. subsumption
      Strict priorities
      Behavior proliferation
      Easy to construct
  Relative priority – dynamic priorities based on input determine winner
    E.g. activation-based
      Fewer behaviors
      Harder to design
Behavior
Activation
Control

## Slide 15: Behavior-Based Architectures
Cooperative composition mechanisms
  Additive – All behaviors add together to drive system
    E.g. schema-based
      Emergent behavior
      Fewer behaviors
      Difficult to predict

## Slide 16: Hybrid Deliberative/Reactive Control
To get the best of both worlds, UxVs often combine deliberative and reactive control
    Abstract task planning layer
        Deliberative decisions
        Plans goal directed policies based on environment models
    Reactive behavior layer
        Provides reactive actions
        Handles sensors and actuators

## Slide 17: Hybrid Deliberative / Reactive Control
Hybrid deliberative / reflexive architectures plan tasks at a more abstract level
  Planning in terms of reactive behaviors
    Allows to ignore details of the state during planning
    Reduces the likelihood that the system deviates from the plan
    Decomposes plans from low level aspects of the environment
  Behavior layer operates system in environment
    Fast reaction to changes
    Bridges time needed to update plan

## Slide 18: Hybrid Deliberative/Reactive Control
Hybrid architectures can yield autonomy at both the task and the local control level

## Slide 19: Traditional and Behavior Based Control
Traditional control methods have a bottleneck in the form of a complete world model
  E.g. Path planning requires complete world knowledge
  Modifications to the model requires replanning
    Very high overhead
    No knowledge of correct activity during replanning
Behavior Based control attempts to solve tasks using a set of simpler controllers
  Can be designed to react to unexpected situations
    Have problems with complex tasks
Hybrid architectures can combine both